## Slide 1
Subjects’ Traces alignment
Andrea Corrado
August 2024

## Slide 2: Outline
Necessity of alignment
QRS detection: Pam-Tompinks algorithm
Traces alignment: strategy 1
  Description
  Results
Traces alignment: strategy 2
  Description
  Results
Conclusions

## Slide 3: Outline
Necessity of alignment
QRS detection: Pam-Tompinks algorithm
Traces alignment: strategy 1
  Description
  Results
Traces alignment: strategy 2
  Description
  Results
Conclusions

## Slide 4: Necessity of Alignment
So far, we encountered several problems:
Distinguish between atrial and ventricular components into the ROV trace is not so easy
Traces are not directly comparable due to difference into the positions of the peaks
Population analysis isn’t possible in such situation
Atrial? Ventricular?
It’s necessary to find out a way to align traces
Key idea: align respect to QRS
QRS
Atrial
Ventricular

## Slide 5: Pseudo-code strategy
To align Rov signals respect to the QRS the following strategy is used:
For each Rov signal
  Find the QRS into another trace (i.e., reference or spare)
  Define into the ROV trace a neighbourhood into which there is the QRS
  Find the peak into the neighbourhood of the Rov trace
  Align the QRS with the Rov peak using Nan-Padding and maintaining the original length of the signal.
QRS detection
Rov Neighborhood definition
Maximum into neighborhood localization
Peaks alignment

## Slide 6: Outline
Necessity of alignment
QRS detection: Pam-Tompinks algorithm
Traces alignment: strategy 1
  Description
  Results
Traces alignment: strategy 2
  Description
  Results
Conclusions

## Slide 7: Pam-Tompkins algorithm
The Pan-Tompkins algorithm, (Willis J. Tompkins and Jiapu Pan, 1985) was designed to accurately detect QRS complexes in electrocardiogram (ECG) signals in real-time.
The algorithm works through a series of steps:
Bandpass Filtering: It filters the ECG signal to remove noise and baseline drift, focusing on the QRS complex frequency range (5-15 Hz).
Differentiation: The filtered signal is differentiated to highlight the high slopes of the QRS complex, which are its most distinctive feature.
Squaring: The differentiated signal is squared to accentuate the large values and suppress smaller ones, enhancing the QRS complex peaks.
Moving Window Integration: This step smooths the squared signal, producing a waveform that shows prominent peaks corresponding to the QRS complexes.
Thresholding: The integrated signal is then compared against a dynamic threshold to detect the precise QRS complex locations.
This algorithm is highly effective and has become a standard method for QRS detection due to its accuracy and relatively low computational complexity, making it suitable for real-time applications.

## Slide 8: Outline
Necessity of alignment
QRS detection: Pam-Tompinks algorithm
Traces alignment: strategy 1
  Description
  Results
Traces alignment: strategy 2
  Description
  Results
Conclusions

## Slide 9: Traces alignment: strategy 1
For each signal:
On the reference signal find the QRS position
Then switch to the Rov signal:
  Define a neighbourhood which contains the QRS position (i.e., QRS is the center)
  Where is the window of time into which searching for the maximum
  Find the maximum of the neighbourhood
  Compute the distance:
  If the distance is negative:
    The QRS is before the maximum  Nan-padding at the end of the signal
  If the distance is positive
    The QRS is after the maximum  Nan-padding on top of the signal
Hyperparameters
Time window: 0.01 s

## Slide 10: Strategy 1: results
For some traces results are encouraging.
  Clear distinction between atrial and ventricular components (and His’ bundle)
  Division of components in accordance with the expected characteristics of MAPs
In other cases, the results are misleading
  Atrial signal aligned with the QRS, while the ventricular one not.
MAP A
MAP B
MAP C
MAP A
MAP B
MAP C

## Slide 11: Strategy 1: understanding misleading results
Looking deeper is possible to recognize a sort of pattern into signals with misleading results.
Not correctly aligned
Correctly aligned
Not correctly aligned
Correctly aligned
Not correctly aligned
Correctly aligned
When the ROV signal is not correctly aligned, even the spare2 trace is not
Is it possible that Ref traces are aligned with an ungiven rule? I.e., by centering the QRS into the 1-second –length acquisition?
Previous analysis suggest yes
It’s necessary find out a way to consider such situation when defining the neighborhood

## Slide 12: Outline
Necessity of alignment
QRS detection: Pam-Tompinks algorithm
Traces alignment: strategy 1
  Description
  Results
Traces alignment: strategy 2
  Description
  Results
Conclusions

## Slide 13: Traces alignment: strategy 2
For each signal:
Find the QRS position on the reference signal and on the spare 2 one.
Then switch to the Rov signal:
  Evaluate the time delay between the QRS position into Rov and spare 2 trace.
  If the Delay is more than a certain :
    QRS points are not close in time  center the neighbourhood around the QRS of the spare 2 trace
  If the Delay is lower than a certain :
    QRS into spare 2 trace is near the QRS into the reference trace  center the neighbourhood around the QRS of the reference
  Define a neighbourhood which contains the QRS position (i.e., QRS is the center)
  Where is the window of time into which searching for the maximum
  Find the maximum of the neighbourhood
  Compute the distance:
  If the distance is negative:
    The QRS is before the maximum  Nan-padding at the end of the signal
  If the distance is positive
    The QRS is after the maximum  Nan-padding on top of the signal
Hyperparameters
Time window: 0.01 s
Tolerance: 0.05 s
Notes:
the possibility of having multiple QRS detected is handle considering the most prominent one
Unvaluable QRS points are imputed using the median QRS position for the trace

## Slide 14: Strategy 2: results
Results correctly obtained with strategy 1 are maintained.
But now errors are corrected.
  Clear distinction between atrial and ventricular components (and His’ bundle) even in signals with spare traces not aligned respect to the reference
  Even with signals with multiple QRS episodes
Even if not always
  Due to limits of the QRS-detection algorithm. (i.e., low flexibility of hyperparameters)
  A visual inspection suggest less than 1.5% of signals bad aligned
Strategy 1
Strategy 2
Strategy 2
Strategy 2
Strategy 2

## Slide 15: Further comments and observations
After the alignment it’s possible to clearly distinguish between atrial and ventricular contributions.
Thus, it’s possible to check the Maps’ proprieties.
By looking at the signals after the alignment there is still an open question:
Why some traces have a dominant component which is not expected?
Example: dominant ventricular signal into a record from MAP A
Possible answers:
Wrong strategy of alignment
Noise and bad positioning of the electrode
Necessity of positional information to completely characterize the signal (i.e., the heart surgeon knows where it’s located with the electrode and uses this information to “classify” the signal)
Since the classification is done a posteriori (knowing the ablation result), it is possible that the signal may be afferent to a certain MAP even though its characteristics do not suggest the classification assigned to it
Why?

## Slide 16: Outline
Necessity of alignment
QRS detection: Pam-Tompinks algorithm
Traces alignment: strategy 1
  Description
  Results
Traces alignment: strategy 2
  Description
  Results
Conclusions

## Slide 17: Conclusions
The presented analysis starts by highlighting the necessity of signal alignment
The first strategy used was too simple and leads to misleading results
The second one considers even of the spare signals, leading to more robust and reliable results. Even in this case some errors can occur but are very limited (less than 1.5% of signals). Probably, a more flexible and adaptable algorithm could improve the overall quality of the alignment
Finally, an analysis of the information lost due to Nan-Padding should be done:
On average, each subject lost 10% of each signal record (around 200 points per signal)
But such average has high standard deviation: around 7% (maximum average information lost: 15%, lowest: 0.3%)