## Slide 1
Envelope analysis
Andrea Corrado
October 2024

## Slide 2: Envelope definition
Envelope has been computed for each signal with the Root Mean Square method with a window of 30 points:
Basically, this is a moving average on N points, each of them squared.
The window length has been fixed empirically by comparing different lengths and choosing the one which seems to a be the best compromise between envelope smoothness and peaks resolution.
The aim of this analysis is finding envelope peaks, which are related to active parts of the signals, and finding the corresponding time windows.

## Slide 3: Envelope analysis: derivative computation
The aim of this analysis is finding envelope peaks, which are related to active parts of the signals, and finding the corresponding time windows.
A first step could be analysing the derivative of the envelope:
Where the envelope is going up
Where the envelope is going down
So, when the derivative shows a sign change, probably these is a peak into the signal.
To compute the derivative of the envelope:
Original envelope has been smoothed using a moving average (N=30)
Signal edges (t<0.15 s and t>0.6 s) have been removed because is known are misleading.
The derivative has been approximated as the difference:
Finally, even the derivative has been smoothed using a moving average on N=50 points to clean the curve from spurious peaks.

## Slide 4: Envelope analysis: derivative thresholding
Once the derivative has been computed, finding where the curve is positive or negative is necessary.
To do it, a symmetric threshold, has been defined.
With the defined threshold two logical maps have been defined:
Map_upper: points of positive derivative
Map_lower: points of negative derivative
These maps are made of runs of 1 and 0 and, from now on, a single run of the map_upper will be called “positive runs”, and a single run of map_lower will be called “negative runs”.
Then, inadmissible areas have been merged or removed according to these criterions:
Two (ore more) positive runs not interrupted by a negative one are part of the same ascent, thus can be merged. The same is done with runs of map lower not interrupted by a positive run.
Because the envelope has only positive peaks, no peak can begin with a negative derivative and end with a positive derivative, so negative runs not preceded by a positive and positive runs not followed by a negative are removed

## Slide 5: Envelope analysis: false peak detection
There is the possibility of false peaks:
Peaks not representative
Small deflections part of a higher peak
A possibility could be removing negative runs which satisfy:
Where the must be set such that if the minimum is less than it then it is probably close to the global minimum of the envelope.
A first idea is considering extinct a peak if the minimum of the negative run is lower then, for example, the 10% of the maximum of the envelope.
But results could be misleading and sensible to threshold definition.
These results are still incomplete, and the pipeline require optimization.

## Slide 6: Envelope analysis: time threshold definition
Finally, time threshold can be computed easily:
First point of each positive run begins an active portion
Last point of each negative run ends the active portion

## Slide 7: MAP A: positive result

## Slide 8: MAP B: positive result

## Slide 9: MAP C: positive result

## Slide 10: MAP A: misleading result

## Slide 11: MAP B: negative result

## Slide 12: MAP C: misleading result

## Slide 13: Conclusions
…
Peak cleaning tbc
  Sometimes threshold seem to be too low, leading to “false negative” peaks
  But in other cases seems to be too high, leading to “false positive” peaks
  In both cases the problem is related to signal amplitude, more complete evaluation should be done.
Pros
  Automated time-windows definition
  High sensibility even to small peaks
Cons
  High sensibility to the thresholds used
Feature definition
  Peak ordered by magnitude
  Or by location
  Other features? Like duration of active areas, time elapsed between them and so on