## Slide 1
Heuristic classifier
Andrea Corrado
October 2024

## Slide 2: Outline
Why building a heuristic classifier
Knowledge on roving signals: recap
Heuristic classifier: pseudo code
Performance
Conclusions

## Slide 3: Outline
Why building a heuristic classifier
Knowledge on roving signals: recap
Heuristic classifier: pseudo code
Performance
Conclusions

## Slide 4: Why building a heuristic classifier
Problem
Which model could act as baseline for building and comparing any other one?
In literature there’s no evidence of AVNRT roving signals classification
Proposed solution
So, a first classifier, which could cover this role, could be a heuristic one based on the expectations on these signals
Aim
Building a logical set of rules to classify roving signals exploiting the expectations on them

## Slide 5: Outline
Why building a heuristic classifier
Knowledge on roving signals: recap
Heuristic classifier: pseudo code
Performance
Conclusions

## Slide 6: Knowledge on roving signals: recap
Map A
Amplitude >0.5 mv
Simple and biphasic shape of atrial wave
No slow-path signal
Minor presence of the Ventricular component
Map B
Complex atrial component within 0.1 and 0.3 mV
Higher ventricular component
Map C
3 components: atrial activity, ventricular activity and His Bundle passage
Not fixed proportions between atrial and ventricular components
Clear and biphasic atrial component

## Slide 7: Knowledge on roving signals: recap
Map A
Amplitude >0.5 mv
Simple and biphasic shape of atrial wave
No slow-path signal
Minor presence of the Ventricular component
ECG 1
ECG 1
ECG 2
ECG 3

## Slide 8: Knowledge on roving signals: recap
Map B
Complex atrial component within 0.1 and 0.3 mV
Higher ventricular component
ECG 2
CS 3-4
ECG aVF
ECG V1

## Slide 9: Knowledge on roving signals: recap
Map C
3 components: atrial activity, ventricular activity and His Bundle passage
Not fixed proportions between atrial and ventricular components
Clear and biphasic atrial component
ECG 1
ECG 1
ECG 2
ECG 3

## Slide 10: Outline
Why building a heuristic classifier
Knowledge on roving signals: recap
Heuristic classifier: pseudo code
Performance
Conclusions

## Slide 11: Heuristic classifier: pseudo code
For each roving trace (post-alignment):
Divide the trace in three segments:
  Atrial: before t=0.35s
  Ventricular: after t=0.5
  His bundle: 0.35<t<0.5
Into each segment find, if there is, the main peak
  Usage of find_peaks (python) with prominence set as a multiple of the SD of the segment, by trial and errors fixed at 6 times SD
Then apply the following set of rules:
Does the signal have an His peak?
Does the signal have an atrial peak higher than ventricular one?
MAP C
MAP A
MAP B
No
No
Yes
Yes
Applied on both filtered and not filtered signals
NB: in this way MAP_B, effective, is chosen only if both the two antecedent conditions are satisfied, so is harder to be chosen, leading to a more “conservative” algorithm, as is should be the surgeon

## Slide 12: Outline
Why building a heuristic classifier
Knowledge on roving signals: recap
Heuristic classifier: pseudo code
Performance
Conclusions

## Slide 13: Heuristic classifier: results
Performance have been evaluated using confusion matrix and standard metrics

## Slide 14: Heuristic classifier: results
 | Precision | Recall | F1-score | support
Map A | 0.77 | 0.55 | 0.64 | 796
Map B | 0.10 | 0.35 | 0.16 | 120
Map C | 0.57 | 0.25 | 0.34 | 122
Accuracy |  |  | 0.49 | 1038
Macro avg | 0.48 | 0.38 | 0.38 | 1038
Weighted avg | 0.67 | 0.49 | 0.55 | 1038

## Slide 15: Outline
Why building a heuristic classifier
Knowledge on roving signals: recap
Heuristic classifier: pseudo code
Performance
Conclusions

## Slide 16: Conclusions
A heuristic classifier has been built with the purpose to act as baseline from which starting further evaluations.
In general:
Map A is classified fairly well, with an f1-score of 0.64, indicating sufficient performance
Map B and C are bad classified, with a very low f1-score. This leads to the conclusion that the heuristic classifier does not correctly classify these classes, with a high rate of positive samples misclassified or with high rate of false positive.
Moreover, filtered data does not have difference with not filtered ones in terms of performances.
In conclusion the presented set of rules is a simple classifier, which can be used as baseline to start the classification with a true machine learning model.