## Slide 1
Results of data exploration
Andrea Corrado
July 2024

## Slide 2: Outline
Data summary and overview
Evaluations on data as population
Evaluation of a priori know characteristics of Rov trace
Comparisons between signals in time domain
Comparisons between signals in frequency domain
Results and Open questions

## Slide 3: Outline
Data summary and overview
Evaluations on data as population
Evaluation of a priori know characteristics of Rov trace
Comparisons between signals in time domain
Comparisons between signals in frequency domain
Results and Open questions

## Slide 4: Data summary and overview
Data hierarchy
MAP A
MAP B
MAP C
For each map, 12 Subjects
For each subject, 5 Traces
Rov
Ref
Spare 1 (Ref)
Spare 2
Spare 3
180 Traces
 | Number of records for subjects and maps |  |  |  |  |  |  |  |  |  |  | 
Sub | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
MAP A | 97 | 78 | 80 | 193 | 80 | 256 | 11 | 18 | 7 | 11 | 18 | 27
MAP B | 11 | 5 | 22 | 20 | 22 | 14 | 6 | 9 | 7 | 5 | 3 | 18
MAP C | 5 | 7 | 16 | 32 | 16 | 11 | 2 | 11 | 5 | 4 | 5 | 24
Fc: 2035Hz
Time duration: 1 s
Each trace has the same number of signals collected, which differs within maps and subjects
Basic observations:
MAP A has on average 73 records for patient in each trace, while for MAP B there are 12 traces and for MAP C 11.
On average, in MAP B the traces have 65% less records compared with MAP A. For MAP C such reduction reaches the 70%.
The dataset is clearly unbalanced.
For each MAP we have (1156 total records):
  MAP A: 876 records
  MAP B: 142 records
  MAP C: 138 records

## Slide 5: Outline
Data summary and overview
Evaluations on data as population
Evaluation of a priori know characteristics of Rov trace
Comparisons between signals in time domain
Comparisons between signals in frequency domain
Results and Open questions

## Slide 6: MAP A: Population analysis, expectations
Rov trace expected characteristics:
Amplitude >0.5 mv
Simple and biphasic shape
No slow-path signal
Minor presence of the Ventricular component
MAP A: indifferent signals
Note: figure represents an ideal case

## Slide 7: MAP A: Unexpected behaviors
Rov Trace unexpected behaviors
Amplitude slower than 0.5 Mv (on average)
Shape not clearly “simple and biphasic”
Appreciable presence of ventricular signal
Presence of slow path signal

## Slide 8: MAP B: Population analysis, expectations
Rov trace expected characteristics:
Complex atrial component within 0.1 and 0.3 mV
Higher ventricular component
MAP B: effective signals
Note: figure represents an ideal case

## Slide 9: MAP B: Unexpected behaviors
Rov Trace unexpected behaviors
Presence of appreciable atrial contribution
Presence of unclear components before the atrial one

## Slide 10: MAP C: Population analysis, expectations
Rov trace expected characteristics:
3 components: atrial activity, ventricular activity and His Bundle passage
Not fixed proportions between atrial and ventricular components
Clear and biphasic atrial component
MAP C: dangerous signals
1
2
3
Note: figure represents an ideal case

## Slide 11: MAP C: Unexpected behaviors
Rov Trace unexpected behaviors
Three components not clearly visible (even looking at confidence intervals)
Presence of components before the atrial contribution
Peaks with unphysiological values
?

## Slide 12: First observations
These first evaluation made using all available signals as a sort of “population” highlights some crucial aspects:
In all MAPs appear appreciable and not expected contributions, even the “smoothing” action of the mean.
In MAP C the “His bundle” contribution is not visible even by looking at the confidence intervals. But other visualizations open a possibility (figure on the right).
These observations, in addition to the ones made before, leads to a question: does the signals need to be aligned? In case, which is the criterion?

## Slide 13: Outline
Data summary and overview
Evaluations on data as population
Evaluation of a priori know characteristics of Rov trace
Comparisons between signals in time domain
Comparisons between signals in frequency domain
Results and Open questions

## Slide 14: MAP A: Expectations
Rov trace expected characteristics:
Amplitude >0.5 mv
Simple and biphasic shape
No slow-path signal
Minor presence of the Ventricular component
MAP A: indifferent signals

## Slide 15: MAP A: Unexpected behaviors
Rov Trace unexpected behaviors
Amplitude slower than 0.5 Mv
Shape not always “simple and biphasic”
Appreciable presence of ventricular signal
Presence of slow path signal

## Slide 16: MAP B: Expectations
Rov trace expected characteristics:
Complex atrial component within 0.1 and 0.3 mV
Higher ventricular component
MAP B: effective signals

## Slide 17: MAP B: Unexpected behaviors
Rov Trace unexpected behaviors
Very noisy signals
Presence of spurious components at the beginning of the signal
(TBC) presence of MAP A signals

## Slide 18: MAP C: Expectations
Rov trace expected characteristics:
3 components: atrial activity, ventricular activity and His Bundle passage
Not fixed proportions between atrial and ventricular components
Clear and biphasic atrial component
MAP C: dangerous signals
1
2
3

## Slide 19: MAP C: Unexpected behaviors
Rov Trace unexpected behaviors
Not so clear and biphasic atrial signal
(TBC)Not always present 3 components
(TBC) possible presence of signals of other maps

## Slide 20: Outline
Data summary and overview
Evaluations on data as population
Evaluation of a priori know characteristics of Rov trace
Comparisons between signals in time domain
Comparisons between signals in frequency domain
Results and Open questions

## Slide 21: Comparisons between signals [1/3]
In general, clear difference of amplitude between signals
Expected behaviors of Rov trace confirmed between maps, at least in most cases.
Differences into the alignment of the peaks, even between signals of the same subject.
Comparisons between (mean) signals of different subjects
Map A example
Map B example
Map C example
Should these signals be aligned respect to the P wave?

## Slide 22: Comparisons between signals [2/3]
Rov trace:
  in general, maps behaviors confirmed
  High variability in amplitude of signals
  (TBC) Alignment issues
Ref/spare 1 trace:
  Minor differences between maps, most relevant related to the expected components of the signals
Spare 2 trace:
  Minor differences between maps Signals are in general less clear and interpretable.
Spare 3 trace:
  Minor differences between maps. Signals clearer and more interpretable.
Subject signals variability
Map A, Rov trace
Map B, Rov trace
Map C, Rov trace
Map C, Ref trace
Map B, Ref trace
Map A, Ref trace
Map C, spare2 trace
Map B, spare2 trace
Map A, spare2 trace
Map C, spare3 trace
Map B, spare3 trace
Map A, spare3 trace

## Slide 23: Comparisons between signals [3/3]
Comparisons between maps for the same (mean) signal
Rov trace:
  In general, clear difference between maps components
  Even if not in all cases
Ref/spare 1 trace:
  Certain overlapping between maps
  High variability in the shape between subjects
Spare 2 trace:
  Certain overlapping between maps
  High variability in the shape between subjects
Spare 3 trace:
  Certain overlapping between maps
  High variability in the shape between subjects

## Slide 24: Outline
Data summary and overview
Evaluations on data as population
Evaluation of a priori know characteristics of Rov trace
Comparisons between signals in time domain
Comparisons between signals in frequency domain
Results and Open questions

## Slide 25: Methods: spectrum estimation
Spectrum estimation through AR model
Spectrum of the target signal
Spectrum of ARMA model
Spectrum of the input signal of the model (white noise)
Transfer function of the AR model which approximates the ARMA one
ARMA models can be approximated by an AR with sufficiently high order
Fast and easy application
Consistent estimation of the spectrum
Order choice is crucial

## Slide 26: Methods: order evaluation
Order choosing is done using the AIC criterion into the following pseudo-code:
For each candidate order
  Evaluate a model on the signal:
  Evaluate the AIC of the model:
  Compare the AIC with the previous one:
    If the difference is lower than a certain save the order as the optimal one, otherwise continue.
    If the difference never become lower than , consider the best order as the one corresponding to the lower AIC.
Then use the optimal order to evaluate the spectrum.
AIC by order
Spectrogram example
AR example

## Slide 27: Comparisons between signals, frequency domain [1/3]
Spectrum information sparser for Rov trace, while for other traces is more concentrated into lower frequences.
In some cases, even the Ref/Spare 1 trace is sparser like the Rov one.
Spectrum in general limited at least at 200Hz, as can be expected from previous studies.
Comparisons between (mean) signals spectrums of different subjects
Map A example
Map B example
Map C example

## Slide 28: Comparisons between signals, frequency domain [2/3]
Rov trace:
  Amplitude of components comparable for the same subject
  As expected, MAP C has sparser frequency components because of the higher complexity of these signals
Ref/spare 1 trace:
  Most of information into the 0-30Hz band, where amplitudes are still comparable
  For some subjects there is a higher distribution of the components
Spare 2 trace:
  Quite difficult distinguish between maps just by looking at spectrums.
  Components between 0 and 40Hz.
Spare 3 trace:
  Quite difficult distinguish between maps just by looking at spectrums.
  In some cases, sparser components
Subject signals (mean) spectrums variability
Map A, Rov trace
Map B, Rov trace
Map C, Rov trace
Map C, Ref trace
Map B, Ref trace
Map A, Ref trace
Map C, spare2 trace
Map B, spare2 trace
Map A, spare2 trace
Map C, spare3 trace
Map B, spare3 trace
Map A, spare3 trace

## Slide 29: Comparisons between signals, frequency domain [3/3]
Comparisons between maps for the same (mean) signal spectrum
Rov trace:
  Not clear differences between maps in term of frequency components separability
  Certain variability between amplitudes
Ref/spare 1 trace:
  Overlapping between maps
  Considerable variability between subjects in terms of frequency components distribution and amplitude, but these difference persist between maps, making them not clearly distinguishable
Spare 2 trace:
  Overlapping between maps
  In general, spectrum concentrated between 0 and 40Hz independently from maps
Spare 3 trace:
  Overlapping between maps
  In general, spectrum concentrated between 0 and 40Hz independently from maps

## Slide 30: Outline
Data summary and overview
Evaluations on data as population
Evaluation of a priori know characteristics of Rov trace
Comparisons between signals in time domain
Comparisons between signals in frequency domain
Correlation analysis between maps
Results and Open questions

## Slide 31: Results and open questions
Results
Time domain suggest differences between maps for the Rov trace. On the other hand, other signals does not differ so much between maps, while differs within subjects.
Frequency domain confirms that the Rov trace is, in general, richer of high frequency components, while low frequency components are more represented in other traces.
Open questions
Does the signals need to be aligned respect to a certain component of the reference (i.e., P wave)?
Which is the nature of “spare” signals? Are they bipolar derivations or aVR, aVF, and aVL?
Is possible a misclassification of some signals?
How to be sure about the components of the signals? How can we distinguish clearly between atrial and ventricular components?
Is it acceptable the variable founded into the shape of reference signals?
Is what I found in agreement with the expectations on these signals?
Are there some analysis that worth to be done in addition to the ones done so far?
Are there some important considerations that I missed?

## Slide 32: Correlation Analysis
As probably the most interesting trace is the Rov trace, correlation analysis is done on this trace.
Scope: find if Rov traces (mean) are correlated between maps.
Method:
  coefficient is evaluated for each map pair (A-B, A-C, B-C) and collected for each subject. As result we get 3 vectors of .
  Boxplots of distribution are then built for these vectors
  Paired T-Test between vectors are done to assess differences
Results:
  From boxplot is appreciable the different distribution between . Maps A-B seems to positively correlated in some cases, while comparisons with map C return an overall lower correlation, suggesting that maps A and B are less correlated with map C.
  T-Test results suggest that the correlation between maps A-B and B-C is significantly different, which agrees with considerations made before. On the other hand, other cases does not evidence significant differences. It worth to be noted that even if between A-B and B-C are not significantly different, p-value is low.
t-test | (A-B) vs (A-C) | (A-B) vs (B-C) | (B-C) vs (A-C)
Null HP | 0 | 1 | 0
p-value | 0,098 | 0,047 | 0,47
 | (A-B) vs (A-C) | (A-B) vs (B-C) | (B-C) vs (A-C)
Null HP | 0 | 1 | 0
p-value | 0,098 | 0,047 | 0,47