## Slide 1
Features extraction and classification
Andrea Corrado
November 2024

## Slide 2: Outline
Feature extraction
  Envelope features
  Template matching features
  Short time Fourier transformation features
Classification
  Knowledge based classifier: recap
  Improved Knowledge based classifier
  Tree classifier: whole set of features optimal subset of features
Conclusions

## Slide 3: Outline
Feature extraction
  Envelope features
  Template matching features
  Short time Fourier transformation features
Classification
  Knowledge based classifier: recap
  Improved Knowledge based classifier
  Tree classifier: whole set of features optimal subset of features
Conclusions

## Slide 4: Envelope definition and peak recognition
The aim of the analysis finding where a signal has active areas using RMS envelope:
The window length has been fixed empirically to N=30.
The proposed analysis pipeline is made of 3 main steps (signal has been windowed between 0.17 and 0.6 seconds.):
Envelope derivative computing:
Derivative thresholding  finding slope changes and defining logical maps of positive and negative derivative:
NB: Asymmetric threshold
Time thresholds of active areas definition  boundaries of maps are the begin and the end of active areas.

## Slide 5: The over-detecting problem
This pipeline has, by building, a peculiarity: active areas are found in superabundance. In fact:
high sensibility of the upper threshold  even noise could be detected as peak  even noise can be seen as “active area”
In other words, this pipeline works with the logic “the higher, the better”. A decisional rule is necessary.
Thus:
True active areas are the ones associated to peaks higher than K=2.5 times the standard deviation of the signal.
After time thresholds cleaning

## Slide 6: Features set 1.1: signal peak in order of magnitude
MAP_A has:
- 8 signals with one active area
- 452 signals with two active areas
- 180 signals with three active areas
- 23 signals with more than three active areas
total : 640
MAP_B has:
- 0 signals with one active area
- 67 signals with two active areas
- 26 signals with three active areas
- 1 signals with more than three active areas
total : 93
MAP_C has:
- 0 signals with one active area
- 20 signals with two active areas
- 62 signals with three active areas
- 8 signals with more than three active areas
total : 82
Prior Knowledge
Unclear behaviour

## Slide 7: Features set 1.2: Signal peaks in order of time occurrence
MAP_A has:
- 8 signals with one active area
- 452 signals with two active areas
- 180 signals with three active areas
- 23 signals with more than three active areas
total : 640
MAP_B has:
- 0 signals with one active area
- 67 signals with two active areas
- 26 signals with three active areas
- 1 signals with more than three active areas
total : 93
MAP_C has:
- 0 signals with one active area
- 20 signals with two active areas
- 62 signals with three active areas
- 8 signals with more than three active areas
total : 82

## Slide 8: Active area analysis: entire set of features
Starting from active areas definition other features have been computed:
Number of active area detected
Signal and envelope peaks absolute values
  In order of magnitude: Dominant, Subdominant, Minor peak value and time (6 features + 6 features from envelope signal)
  In order of occurrence: First, Second, Third peak value and time (6 features + 6 features from envelope signal)
Duration of active signal
Silent phase within signal duration
Ratios between single features
  Subdominant to major,
  Minor to subdominant
  Atrial to ventricular peak ratio
  Atrial to ventricular peak time ratio
  Number of active areas on duration ratio
  Silent phase on duration ratio
  Number of peaks on duration ratio

## Slide 9: Outline
Feature extraction
  Envelope features
  Template matching features
  Short time Fourier transformation features
Classification
  Knowledge based classifier: recap
  Improved Knowledge based classifier
  Tree classifier: whole set of features optimal subset of features
Conclusions

## Slide 10: Template matching definition
The aim of the analysis is finding where a signal has a “simple and biphasic” behaviour rather than a more complex one.
Template definition:
TM1: single period of length T=0.05 seconds of a biphasic wave.
TM2: single period of length T=0.1 seconds of a complex-shaped wave.
The cross-correlation signal has been computed as convolution between the template (reversed) and the roving signal:
Where both roving trace and template have been normalised to exclude the amplitude contribution to the cross-correlation signal.
Then, the peak (in modulus) of cross-correlation, its location and the energy of the cross-correlation signal have been used as features from both templates.

## Slide 11: Features set 2: Template Matching features
MAP_A has:
- 8 signals with one active area
- 452 signals with two active areas
- 180 signals with three active areas
- 23 signals with more than three active areas
total : 640
MAP_B has:
- 0 signals with one active area
- 67 signals with two active areas
- 26 signals with three active areas
- 1 signals with more than three active areas
total : 93
MAP_C has:
- 0 signals with one active area
- 20 signals with two active areas
- 62 signals with three active areas
- 8 signals with more than three active areas
total : 82
TM1
TM2

## Slide 12: Outline
Feature extraction
  Envelope features
  Template matching features
  Short time Fourier transformation features
Classification
  Knowledge based classifier: recap
  Improved Knowledge based classifier
  Tree classifier: whole set of features optimal subset of features
Conclusions

## Slide 13: STFT definition
The aim of the analysis is finding if signals have different time-frequency behaviours across classes.
Short Time Fourier Transformation has been evaluated on roving signals to obtain a 2-dimensional representation.
STFT is defined as:
Where:
is the Hamming window of length M=64, centred into m. The overlapping between windows has been fixed as 30%.
The main problem with STFT is that in literature is widely used as input of deep-learning algorithms. Thus, average power features have been defined from scratch:
For each peak detected in order of magnitude [and occurrence]:
  Average Power into low frequency sub-band: 0-75 Hz
  Average Power into medium frequency sub-band: 75-150 Hz
  Average Power into high frequency sub-band: 150-350 Hz
Where the average power have been defined as average of the pixel into the corresponding window detected.

## Slide 14: Features set 3.1: Avg LF Power of peaks
MAP_A has:
- 8 signals with one active area
- 452 signals with two active areas
- 180 signals with three active areas
- 23 signals with more than three active areas
total : 640
MAP_B has:
- 0 signals with one active area
- 67 signals with two active areas
- 26 signals with three active areas
- 1 signals with more than three active areas
total : 93
MAP_C has:
- 0 signals with one active area
- 20 signals with two active areas
- 62 signals with three active areas
- 8 signals with more than three active areas
total : 82
Order of magnitude
Order of occurrence

## Slide 15: Features set 3.1: Avg MF Power of peaks
MAP_A has:
- 8 signals with one active area
- 452 signals with two active areas
- 180 signals with three active areas
- 23 signals with more than three active areas
total : 640
MAP_B has:
- 0 signals with one active area
- 67 signals with two active areas
- 26 signals with three active areas
- 1 signals with more than three active areas
total : 93
MAP_C has:
- 0 signals with one active area
- 20 signals with two active areas
- 62 signals with three active areas
- 8 signals with more than three active areas
total : 82
Order of magnitude
Order of occurrence

## Slide 16: Features set 3.1: Avg HF Power of peaks
MAP_A has:
- 8 signals with one active area
- 452 signals with two active areas
- 180 signals with three active areas
- 23 signals with more than three active areas
total : 640
MAP_B has:
- 0 signals with one active area
- 67 signals with two active areas
- 26 signals with three active areas
- 1 signals with more than three active areas
total : 93
MAP_C has:
- 0 signals with one active area
- 20 signals with two active areas
- 62 signals with three active areas
- 8 signals with more than three active areas
total : 82
Order of magnitude
Order of occurrence

## Slide 17: Outline
Feature extraction
  Envelope features
  Template matching features
  Short time Fourier transformation features
Classification
  Knowledge based classifier: recap
  Improved Knowledge based classifier
  Tree classifier: whole set of features optimal subset of features
Conclusions

## Slide 18: Knowledge based classifier: recap
For each roving trace:
Divide the trace in three regions (Atrial: t<0.38s, His: 0.38<t<0.42 and Ventricular: 0.42<t<0.6);
Compute the absolute value of each region and find the maximum;
Then, apply the following rules:
KB V0: atrial peak thresholding
KB V1: atrial/ventricular ratio (Th: 05)
Is the His Peak above threshold?
MAP C
MAP A
No
No
Yes
Yes
Is the atrial peak > 0.5 mV?
MAP B
Is the His Peak above threshold?
MAP C
MAP A
No
No
Yes
Yes
MAP B
Is the atrial/ventricular peak ratio >threshold?

## Slide 19: KB classifier V0 and V1: previous results
Of 847 signals:
663 are ineffective (MAP A, 78.28%);
94 are effective (MAP B, 11.1%);
90 are dangerous (MAP C, 10.63%);
KB V0: Atrial peak threshold
KB V1: atrial/ventricular ratio, th=0.5
KB V1: atrial/ventricular ratio, th=0.5

## Slide 20: Outline
Feature extraction
  Envelope features
  Template matching features
  Short time Fourier transformation features
Classification
  Knowledge based classifier: recap
  Improved Knowledge based classifier
  Tree classifier: whole set of features optimal subset of features
Conclusions

## Slide 21: Knowledge based classifier with envelope-based features
Is Minor_peak >0.020?
MAP C
MAP A
No
No
Yes
Yes
Is Dominant_peak_time <0.49
MAP B
Is Minor_peak >0.021?
MAP C
MAP A
No
No
Yes
Yes
Is atrial_ventricular_ratio >0.2?
MAP B
For each roving trace, evaluate the corresponding (active areas) features. Then:
KB V2: peaks thresholds and position
KB V3: peaks thresholds and atrial/ventricular

## Slide 22: Knowledge based classifier with envelope-based features
KB V2: peaks thresholds and position
KB V3: peaks thresholds and atrial/ventricular ratio
Of 847 signals:
663 are ineffective (MAP A, 78.28%);
94 are effective (MAP B, 11.1%);
90 are dangerous (MAP C, 10.63%);
KB V2: peaks thresholds and position

## Slide 23: Knowledge based classifier: comparison V2 (improved) and V1 (original)
KB V1: atrial/ventricular ratio, th=0.5
KB V2: peaks thresholds and position
Of 847 signals:
663 are ineffective (MAP A, 78.28%);
94 are effective (MAP B, 11.1%);
90 are dangerous (MAP C, 10.63%);
Respect to KB V1:
Higher precision and less misclassified MAP C and MAP B signals
Slightly increased number of misclassified signals from MAP C to MAP A and for MAP B to MAP A.
KB V2: peaks thresholds and position

## Slide 24: Outline
Feature extraction
  Envelope features
  Template matching features
  Short time Fourier transformation features
Classification
  Knowledge based classifier: recap
  Improved Knowledge based classifier
  Tree classifier: whole set of features optimal subset of features
Conclusions

## Slide 25: Machine learning approach: tree classifier
Machine learning approaches allow to model data with statistical models trained on a set of features.
Tree models are among the most easily explained, therefore the choice felt on them.
Mathematical rules are defined into each node to minimize the impurity of the following level
An “impurity measure” is required
Tuning the depth of the three is required
LOPOCV is used as validation technique
Tree classifiers
Tree 1: whole feature set
Tree 2: relevant feature set
Impurity measure: Cross entropy
Depth: maximising weighted f1 score
Impurity measure: Cross entropy
Depth: maximising weighted f1 score
Cross entropy definition
Weighted F1 score definition

## Slide 26: Feature selection: correlation matrix
To avoid the usage of features correlated between each other, correlation matrix has been computed.
In the following, three blocks of features will be exanimated:
Active areas features
Template Matching features
STFT features

## Slide 27: Correlation matrix: active areas features
The following features have been discharged from analysis:
Dominant_peak_env
Dominant_peak_env_time
Subdominant_peak_env
Subdominant_peak_env_time
Minor_peak_env
Minor_peak_env_time
First_peak_env
First_peak_env_time
Second_peak_env
Second__peak_env_time
Third_peak_env
Third_peak_env_time
Dominant_peak
silent_phase
Directly correlated with signal peaks into active areas
Directly correlated with First Peak
Directly correlated with Silent Ratio

## Slide 28: Correlation matrix: Template Matching features
The following features have been discharged from analysis:
cross_energy_TM1
cross_peak_TM2
cross_peak_time_TM2
cross_energy_TM2
Directly correlated with TM1 features

## Slide 29: Correlation matrix: STFT features
The following features have been discharged from analysis:
Dominant_AvgPowMF
Subdominant_AvgPowLF
Subdominant_AvgPowMF
Minor_AvgPowLF
Minor_AvgPowMF
First_AvgPowLF
First_AvgPowMF
Second_AvgPowLF
Second_AvgPowMF
Third_AvgPowLF
Third_AvgPowMF
Directly correlated with other SFTF based features

## Slide 30: Tree classifier V1: results
Tree 1: whole feature set
Of 847 signals:
663 are ineffective (MAP A, 78.28%);
94 are effective (MAP B, 11.1%);
90 are dangerous (MAP C, 10.63%);

## Slide 31: Tree classifier V2 – subset of features: results
Tree 2: relevant features set
Of 847 signals:
663 are ineffective (MAP A, 78.28%);
94 are effective (MAP B, 11.1%);
90 are dangerous (MAP C, 10.63%);

## Slide 32: Tree classifiers: LOPOCV confusion matrix comparison
Tree 1: whole feature set
Tree 2: relevant feature subset
Of 847 signals:
663 are ineffective (MAP A, 78.28%);
94 are effective (MAP B, 11.1%);
90 are dangerous (MAP C, 10.63%);
Tree 2: relevant feature subset

## Slide 33: Knowledge based or tree? Best models comparison
Tree 2: relevant feature subset
KB V2: peaks thresholds and position

## Slide 34: SHAP analysis on optimal feature subset

## Slide 35: Outline
Feature extraction
  Envelope features
  Template matching features
  Short time Fourier transformation features
Classification
  Knowledge based classifier: recap
  Improved Knowledge based classifier
  Tree classifier: whole set of features optimal subset of features
Conclusions

## Slide 36: Conclusions
Three feature extraction pipelines based on envelope analysis, template matching and STFT have proposed:
Envelope features provides information on active areas of the signal
Template matching features provides information on signal morphology
STFT features provides information on average power across different frequency intervals and between active areas
Then, three models have been evaluated:
An improved Knowledge based model based on envelope features
A decision tree (LOPO cross validation) trained onto the whole feature set
A decision tree (LOPOCV) trained onto an optimized feature set
Results are encouraging but higher performance are required, specially into MAP A/MAP B discrimination. Moreover, tree models, even if still unsatisfactory in terms of absolute performance misclassify MAP A and MAP C signals, which are, from a theoretical point of view, signals that will not be ablated.
It has been shown that active areas features are the most relevant ones, confirmed by both the feature importance analysis and SHAP plots. Secondly, even Template matching features and STFT based ones plays an important role into cases classification.
Future steps, in terms of model, could be using more robust models like SVM, often used in literature.