## Slide 1
Features extraction and classification
Andrea Corrado
November 2024

## Slide 2: Outline
Feature extraction
  Envelope features
  Template matching features
  Short time Fourier transformation definition and analysis
Classification
  Knowledge based classifier: recap
  Improved Knowledge based classifier
  Tree classifier: whole set of features optimal subset of features
Conclusions

## Slide 3: Outline
Feature extraction
  Envelope features
  Template matching features
  Short time Fourier transformation definition and analysis
Classification
  Knowledge based classifier: recap
  Improved Knowledge based classifier
  Tree classifier: whole set of features optimal subset of features
Conclusions

## Slide 4: Envelope definition and peak recognition
The aim of the analysis finding where a signal has active areas. In other words, where the signal present peaks. A first step into this direction could be done using RMS envelope.
The window length has been fixed empirically to N=30.
The proposed analysis pipeline is made of 4 steps:
Envelope derivative computing:
Derivative thresholding  finding slope changes and defining logical maps of positive and negative derivative:
NB: Asymmetric threshold
Time thresholds of active areas definition  boundaries of maps are the begin and the end of active areas.
NB: signal has been windowed between 0.17 and 0.6 seconds.

## Slide 5: The over-detecting problem
This pipeline has, by building, a peculiarity: active areas are found in superabundance. In fact:
high sensibility of the upper threshold  even noise could be detected as peak  even noise can be seen as “active area”
In other words, this pipeline works with the logic “the higher, the better”. A decisional rule is necessary.
Thus:
True active areas are the ones associated to the three main peaks of the signal in descending order of magnitude. Hence, these are the peaks (in modulus) considered as features.
With such definition, a noisy active area can be easily discharged, at least if the signal is not too noisy (but even a less sensible pipeline would be deceived in this case).

## Slide 6: Features defined from envelope analysis
MAP_A has:
- 22 signals with one peak
- 254 signals with two peaks
- 387 signals with three peaks
total : 663
MAP_B has:
- 0 signals with one peak
- 41 signals with two peaks
- 53 signals with three peaks
total : 94
MAP_C has:
- 2 signals with one peak
- 12 signals with two peaks
- 76 signals with three peaks
total : 90
Prior Knowledge
Unclear behaviour

## Slide 7: Envelope analysis: other features
Starting from active areas definition other features have been computed:
Peaks number
Time and position of envelope peaks
Ratios between single peaks (second to major, third to major)
Total duration of signal active area (whole time between begin and end of the active areas)
Atrial to ventricular ratio
Atrial to ventricular peak time ratio
Silent phase (inactive time within the duration time)
Number of peaks to duration ratio
Silent phase to duration ratio

## Slide 8: Outline
Feature extraction
  Envelope features
  Template matching features
  Short time Fourier transformation definition and analysis
Classification
  Knowledge based classifier: recap
  Improved Knowledge based classifier
  Tree classifier: whole set of features optimal subset of features
Conclusions

## Slide 9: Template matching definition
The aim of the analysis is finding where a signal has a “simple and biphasic” behaviour. To do it, the cross-correlated signal between a template and the signal has been evaluated.
Template definition: a single period of length T=0.05 seconds of the sinus function.
Once defined the template the cross-correlation signal has been computed as convolution between the template (reversed) and the roving signal:
Where both roving trace and template have been normalised to exclude the amplitude contribution to the cross-correlation signal.
Then, the peak (in modulus) of cross-correlation, its location and the energy of the cross-correlation signal have been used as features.

## Slide 10: Energy of whole cross signal, atrial and ventricular phases
MAP_A has:
- 22 signals with one peak
- 254 signals with two peaks
- 387 signals with three peaks
total : 663
MAP_B has:
- 0 signals with one peak
- 41 signals with two peaks
- 53 signals with three peaks
total : 94
MAP_C has:
- 2 signals with one peak
- 12 signals with two peaks
- 76 signals with three peaks
total : 90

## Slide 11: Outline
Feature extraction
  Envelope features
  Template matching features
  Short time Fourier transformation definition and analysis
Classification
  Knowledge based classifier: recap
  Improved Knowledge based classifier
  Tree classifier: whole set of features optimal subset of features
Conclusions

## Slide 12: STFT definition
The aim of the analysis is finding if signals have different time-frequency behaviours. To do it, Short Time Fourier Transformation has been evaluated on roving signals to obtain a 2-dimensional representation of them.
STFT is defined as:
Where:
is the Hamming window of length M=64, centered into m. The overlapping between windows has been fixed as 30%.
The main problem with STFT is that in literature is widely used as input of deep-learning algorithms:
there’s a lack of information about the type of features that could be used to describe these images.
Moreover, even ex-novo defined features must be carefully chosen to ensure that they are not duplicative of those already introduced so far

## Slide 13: Outline
Feature extraction
  Envelope features
  Template matching features
  Short time Fourier transformation definition and analysis
Classification
  Knowledge based classifier: recap
  Improved Knowledge based classifier
  Tree classifier: whole set of features optimal subset of features
Conclusions

## Slide 14: Knowledge based classifier: recap
For each roving trace:
Divide the trace in three regions (Atrial: t<0.38s, His: 0.38<t<0.42 and Ventricular: 0.42<t<0.6);
Compute the absolute value of each region and find the maximum;
Then, apply the following rules:
KB V0: atrial peak thresholding
KB V1: atrial/ventricular ratio (Th: 05)
Is the His Peak above threshold?
MAP C
MAP A
No
No
Yes
Yes
Is the atrial peak > 0.5 mV?
MAP B
Is the His Peak above threshold?
MAP C
MAP A
No
No
Yes
Yes
MAP B
Is the atrial/ventricular peak ratio >threshold?

## Slide 15: KB classifier V0 and V1: previous results
Of 847 signals:
663 are ineffective (MAP A, 78.28%);
94 are effective (MAP B, 11.1%);
90 are dangerous (MAP C, 10.63%);
KB V0: Atrial peak threshold
KB V1: atrial/ventricular ratio, th=0.5
KB V1: atrial/ventricular ratio, th=0.5

## Slide 16: Outline
Feature extraction
  Envelope features
  Template matching features
  Short time Fourier transformation definition and analysis
Classification
  Knowledge based classifier: recap
  Improved Knowledge based classifier
  Tree classifier: whole set of features optimal subset of features
Conclusions

## Slide 17: Knowledge based classifier with envelope-based features
Is third peak >0.021?
MAP C
MAP A
No
No
Yes
Yes
Is peak_1_pos<0.49
MAP B
Is third peak >0.021?
MAP C
MAP A
No
No
Yes
Yes
Is atrial_ventricular_ratio >0.09?
MAP B
For each roving trace, use the envelope to evaluate active areas. Then:
Improved KB V0: peaks thresholds and position
Improved KB V1: peaks thresholds and atrial/ventricular ratio

## Slide 18: Knowledge based classifier with envelope-based features
Improved KB V0: peaks thresholds and position
Improved KB V1: peaks thresholds and atrial/ventricular ratio
Of 847 signals:
663 are ineffective (MAP A, 78.28%);
94 are effective (MAP B, 11.1%);
90 are dangerous (MAP C, 10.63%);
Improved KB V0: peaks thresholds and position
Respect to KB V1:
Higher precision for all maps
Less misclassified MAP C and MAP B signals
Slightly increased number of misclassified signals from MAP C to MAP A and for MAP B to MAP A (left column, last 2 boxes)

## Slide 19: Outline
Feature extraction
  Envelope features
  Template matching features
  Short time Fourier transformation definition and analysis
Classification
  Knowledge based classifier: recap
  Improved Knowledge based classifier
  Tree classifier: whole set of features optimal subset of features
Conclusions

## Slide 20: Machine learning approach: tree classifier
Machine learning approaches allow to model data with statistical models trained on a set of features.
Rules and relationships are not a priori fixed
Possible deeper feature relationship evaluation
Possibility of finding new insights on data
…
Tree models are among the most easily explained, therefore the choice felt on them.
Mathematical rules are defined into each node to minimize the impurity of the following level
An “impurity measure” is required
Tuning the depth of the three is required
LOPOCV is used as validation technique
Tree classifiers
Tree 1: whole feature set
Tree 2: relevant feature set
Impurity measure: Cross entropy
Depth: maximising weighted f1 score
Impurity measure: Cross entropy
Depth: maximising weighted f1 score
Cross entropy definition
Weighted F1 score definition

## Slide 21: Feature selection: correlation matrix
To avoid the usage of features correlated between each other, correlation matrix has been computed.
Prior to classification, some features have been re moved according to the correlation matrix:
Envelope peaks values and time
silent_rateo
cross_energy

## Slide 22: Tree classifier V1: results
Tree 1: whole feature set
Of 847 signals:
663 are ineffective (MAP A, 78.28%);
94 are effective (MAP B, 11.1%);
90 are dangerous (MAP C, 10.63%);

## Slide 23: Tree classifier V2 – subset of features: results
Tree 2: relevant features set
Of 847 signals:
663 are ineffective (MAP A, 78.28%);
94 are effective (MAP B, 11.1%);
90 are dangerous (MAP C, 10.63%);

## Slide 24: SHAP analysis on feature subset

## Slide 25: Tree classifiers: LOPOCV confusion matrix comparison
Tree 1: whole feature set
Tree 2: relevant feature subset
Of 847 signals:
663 are ineffective (MAP A, 78.28%);
94 are effective (MAP B, 11.1%);
90 are dangerous (MAP C, 10.63%);

## Slide 26: Knowledge based or tree?
Tree 2: relevant feature subset
Improved KB V0: peaks thresholds and position

## Slide 27: Is the model learning wrong?
What is learned here…
Has an impact here…
…and here

## Slide 28: How to improve learning?
Tree on subs 7->12 and LOPOCV (relevant feature set)
Of 148 signals:
70 are ineffective (MAP A);
38 are effective (MAP B);
40 are dangerous (MAP C);

## Slide 29: Outline
Feature extraction
  Envelope features
  Template matching features
  Short time Fourier transformation definition and analysis
Classification
  Knowledge based classifier: recap
  Improved Knowledge based classifier
  Tree classifier: whole set of features optimal subset of features
Conclusions

## Slide 30: Conclusions
Two feature extraction pipelines based on envelope analysis and template matching have proposed:
Envelope features provides information on peaks positions and active areas of the signal
Template matching features provides information on signal morphology
Moreover, STFT usage has been explored but features have not been evaluated for the time being as they would have to be meticulously defined from scratch. Otherwise, redundant information would be introduced.
Other similar studies used DWT based features (similar to the one introduced with TM), autocorrelation-based features, self-similarity features and complexity-analysis based features.
Then, three models have been evaluated:
An improved Knowledge based model based on envelope features
A decision tree (LOPO cross validation) trained onto the whole feature set
A decision tree (LOPOCV) trained onto an optimized feature set
Results are encouraging but higher performance are required, specially into MAP A/MAP B discrimination.
Future steps could be:
Defining new features based on a second template (more complex)
Computing new features as envelope peaks area, ApEN, Mutual Information
Defining and analyzing spectral/STFT features