## Slide 1
Heuristic classifier, strategy B
Andrea Corrado
October 2024

## Slide 2: Outline
Why building a heuristic classifier
Knowledge on roving signals: recap
Heuristic classifier: pseudo code
Performance
Conclusions

## Slide 3: Outline
Why building a heuristic classifier
Knowledge on roving signals: recap
Heuristic classifier: pseudo code
Performance
Conclusions

## Slide 4: Why building a heuristic classifier
Problem
Which model could act as baseline for building and comparing any other one?
In literature there’s no evidence of AVNRT roving signals classification
Proposed solution
So, a first classifier, which could cover this role, could be a heuristic one based on prior information on these signals
Aim
Building a logical set of rules to classify roving signals exploiting the prior on them

## Slide 5: Outline
Why building a heuristic classifier
Knowledge on roving signals: recap
Heuristic classifier: pseudo code
Performance
Conclusions

## Slide 6: Knowledge on roving signals: recap
Map A: indifferent
Atrial wave amplitude >0.5 mv
Simple and biphasic shape of atrial wave
No slow-path signal
Minor presence of the Ventricular component
Map B: effective
Complex atrial component within 0.1 and 0.3 mV
Higher ventricular component
Map C: dangerous
3 components: atrial activity, ventricular activity and His Bundle passage
Not fixed proportions between atrial and ventricular components
Clear and biphasic atrial component

## Slide 7: Knowledge on roving signals: recap
Map A
Atrial wave amplitude >0.5 mv
Simple and biphasic shape of atrial wave
No slow-path signal
Minor presence of the Ventricular component
ECG 1
ECG 1
ECG 2
ECG 3
Used for building the classifier

## Slide 8: Knowledge on roving signals: recap
Map B
Complex atrial component within 0.1 and 0.3 mV
Higher ventricular component
ECG 2
CS 3-4
ECG aVF
ECG V1
Used for building the classifier

## Slide 9: Knowledge on roving signals: recap
Map C
Clear and biphasic atrial component
3 components: atrial activity, ventricular activity and His Bundle passage
Not fixed proportions between atrial and ventricular components
ECG 1
ECG 1
ECG 2
ECG 3
Used for building the classifier

## Slide 10: Stratified train/test split
Of the 1038 signals into the dataset:
796 are MAP A (76.69%)
120 are MAP B (11.56%)
122 are MAP C (11.75%)
Thus, the following conclusions could be done:
Unbalanced dataset towards MAP A
Stratified train/test splitting is necessary
  Done with a 70-30% split
Total 726
Total 312

## Slide 11: Outline
Why building a heuristic classifier
Knowledge on roving signals: recap
Heuristic classifier: pseudo code
Performance
Conclusions

## Slide 12: Heuristic classifier: pseudo code
For each roving trace (post-alignment):
Divide the trace in three segments:
  Atrial: t<0.38s
  Ventricular: after t>0.42
  His bundle: 0.38<t<0.42
Compute the absolute value of the segment, then into each (modulus) segment find the maximum:
  For atrial and ventricular phase take the maximum as it is
  For His phase, consider the maximum significant if higher than a threshold, otherwise assign NaN to its value
Then apply the following set of rules:
Does the signal have an His peak?
MAP C
MAP A
MAP B
No
No
Yes
Yes
Applied on both filtered and not filtered signals
NB: in this way MAP B, effective, is harder to be chosen, leading to a more “conservative” algorithm, as is should be the surgeon.
MAP A, indifferent, is chosen if the atrial peak is higher than the ventricular one.
Finally, MAP C, dangerous, is chosen as first one if there’s an over-threshold peak into the His bundle.
Is the ventricular peak lower than atrial one?

## Slide 13: Code functioning
The given record is divided into three segments and the modulus is taken
  Atrial phase: abs(record[t=0 : t=0.38])
  Ventricular phase: abs(record[t=0.42 : t=t_end])
  His phase: abs(record[t=0.38 : t=0.42])
Into each segment the maximum is evaluated
His_bundle peak is compared with the threshold
  If his_peak<his_bundle_th  his_peak = NaN
Finally, the three peaks are compared, and the classification is made:
  If not(isnan(his_peak))  MAP_C
  Elif [atrial_peak>vent_peak  MAP_A
  Else  MAP_B

## Slide 14: His threshold tuning
His peak threshold is fixed as a percentile of the distribution of maxima points around the His Peak of the training signals.
To do it:
From each record the modulus of the His segment is taken
  His phase: abs(record[t=0.38 : t=0.42])
  Boundaries are fixed as wide as possible without f1-score reduction.
Then the maximum of the segment is evaluated and saved into a vector of maximum_points
For each class, the F1-score value is evaluated as a function of the threshold, leading to the plot on the right.
  Higher class F1-score combination is reached with a threshold equal to the 75th percentile
Finally, the value of the threshold is saved for being used in the classification phase
In conclusion, the threshold was 0.0377 mV
Threshold position into the distribution

## Slide 15: Outline
Why building a heuristic classifier
Knowledge on roving signals: recap
Heuristic classifier: pseudo code
Performance
Conclusions

## Slide 16: Correctly classified example 1
MAP A correctly classified
The algorithm recognize as majoritarian the atrial peak (in modulus)
Gray lines: his peak searching box. Red lines: his peak threshold

## Slide 17: Correctly classified example 2
MAP B correctly classified
Higher ventricular peak is used to correctly assign this signal to map B.
Gray lines: his peak searching box. Red lines: his peak threshold

## Slide 18: Correctly classified example 3
MAP C correctly classified
His bundle is correctly recognized and used to classify this signal into MAP C.
Gray lines: his peak searching box. Red lines: his peak threshold

## Slide 19: Misclassified example 1
MAP A classified as MAP B
The algorithm captures the uncertainty given by the clear Map B characteristics of the signal
Gray lines: his peak searching box. Red lines: his peak threshold

## Slide 20: Misclassified example 2
MAP C classified as MAP B
Into this signal an His bundle oscillation is not clearly visible. Then, the signal is assigned to MAP B because of the higher ventricular peak
Gray lines: his peak searching box. Red lines: his peak threshold

## Slide 21: Misclassified example 3
MAP C classified as MAP A
Very low overall amplitude of this signal does imply a little His peak. Then, as it wasn’t considered significant, the signal is assigned to MAP A because of the higher atrial peak
Gray lines: his peak searching box. Red lines: his peak threshold

## Slide 22: Heuristic classifier: results on original signals
Performance have been evaluated using confusion matrix and standard metrics

## Slide 23: Heuristic classifier: results on filtered signals
Performance have been evaluated using confusion matrix and standard metrics

## Slide 24: Heuristic classifier: results on train set
 | Precision | Recall | F1-score | support
Map A | 0.95 | 0.38 | 0.54 | 557
Map B | 0.18 | 0.70 | 0.29 | 84
Map C | 0.34 | 0.72 | 0.46 | 85
Accuracy |  |  | 0.45 | 726
Macro avg | 0.49 | 0.60 | 0.43 | 726
Weighted avg | 0.79 | 0.45 | 0.50 | 726

## Slide 25: Heuristic classifier: results on test set
 | Precision | Recall | F1-score | support
Map A | 0.96 | 0.30 | 0.46 | 239
Map B | 0.16 | 0.62 | 0.26 | 36
Map C | 0.35 | 0.70 | 0.50 | 37
Accuracy |  |  | 0.40 | 312
Macro avg | 0.49 | 0.58 | 0.40 | 312
Weighted avg | 0.80 | 0.40 | 0.44 | 312

## Slide 26: Outline
Why building a heuristic classifier
Knowledge on roving signals: recap
Heuristic classifier: pseudo code
Performance
Conclusions

## Slide 27: Conclusions
A heuristic classifier has been built with the purpose to act as baseline from which starting further evaluations.
In general, performance are not satisfying, as it could be imaged.
Looking at the confusion matrices and metrics, in both train and test sets:
MAP A has many FN classified as MAP B, probably due to ambiguous signals present into this class. Only temporal-spatial information is not sufficient to classify these signals properly. This situation is reflected by the good precision juxtaposed, however with low recall.
MAP B il classified well in terms or recall, but suffers of very low precision, because of the presence MAP A misclassified signals.
MAP C has low precision and recall, but at least half signals are correctly classified, leading to the conclusion that the threshold comparison result could be seen as a first hint to recognize these signals, even if clearly not sufficient.
Moreover, filtered data does not have difference with not filtered ones in terms of performances.
The most important advantage of this algorithm is the full explainability of the process. In fact, the significance of the His Bundle peak can be easily explained, differently from what happened when built-in functions.
In conclusion the presented set of rules is a simple classifier, which can be used as baseline to start the classification with a true machine learning model.