## Slide 1
Heuristic classifier
Andrea Corrado
October 2024

## Slide 2: Outline
Why building a heuristic classifier
Knowledge on roving signals: recap
Heuristic classifier: pseudo code
Performance
Conclusions

## Slide 3: Outline
Why building a heuristic classifier
Knowledge on roving signals: recap
Heuristic classifier: pseudo code
Performance
Conclusions

## Slide 4: Why building a heuristic classifier
Problem
Which model could act as baseline for building and comparing any other one?
In literature there’s no evidence of AVNRT roving signals classification
Proposed solution
So, a first classifier, which could cover this role, could be a heuristic one based on prior information on these signals
Aim
Building a logical set of rules to classify roving signals exploiting the prior on them

## Slide 5: Outline
Why building a heuristic classifier
Knowledge on roving signals: recap
Heuristic classifier: pseudo code
Performance
Conclusions

## Slide 6: Knowledge on roving signals: recap
Map A: indifferent
Atrial wave amplitude >0.5 mv
Simple and biphasic shape of atrial wave
No slow-path signal
Minor presence of the Ventricular component
Map B: effective
Complex atrial component within 0.1 and 0.3 mV
Higher ventricular component
Map C: dangerous
3 components: atrial activity, ventricular activity and His Bundle passage
Not fixed proportions between atrial and ventricular components
Clear and biphasic atrial component

## Slide 7: Knowledge on roving signals: recap
Map A
Atrial wave amplitude >0.5 mv
Simple and biphasic shape of atrial wave
No slow-path signal
Minor presence of the Ventricular component
ECG 1
ECG 1
ECG 2
ECG 3
Used for building the classifier

## Slide 8: Knowledge on roving signals: recap
Map B
Complex atrial component within 0.1 and 0.3 mV
Higher ventricular component
ECG 2
CS 3-4
ECG aVF
ECG V1
Used for building the classifier

## Slide 9: Knowledge on roving signals: recap
Map C
Clear and biphasic atrial component
3 components: atrial activity, ventricular activity and His Bundle passage
Not fixed proportions between atrial and ventricular components
ECG 1
ECG 1
ECG 2
ECG 3
Used for building the classifier

## Slide 10: Stratified train/test split
Of the 1038 signals into the dataset:
796 are MAP A (76.69%)
120 are MAP B (11.56%)
122 are MAP C (11.75%)
Thus, the following conclusions could be done:
Unbalanced dataset towards MAP A
Stratified train/test splitting is necessary
  Done with a 70-30% split
Total 726
Total 312

## Slide 11: Outline
Why building a heuristic classifier
Knowledge on roving signals: recap
Heuristic classifier: pseudo code
Performance
Conclusions

## Slide 12: Heuristic classifier: pseudo code
For each roving trace (post-alignment):
Divide the trace in three segments:
  Atrial: t<0.35s
  Ventricular: after t>0.45
  His bundle: 0.35<t<0.45
Compute the absolute value of the segment, then find, if there is, the main peak
  Usage of find_peaks (python, Scy.Py library) with prominence set as a multiple of the SD of the segment, tuned and fixed at 5 times SD
Then apply the following set of rules:
Does the signal have an His peak?
MAP C
MAP A
MAP B
No
No
Yes
Yes
Applied on both filtered and not filtered signals
NB: in this way MAP B, effective, is harder to be chosen, leading to a more “conservative” algorithm, as is should be the surgeon.
MAP A, indifferent, is chosen even if the rules are not fully satisfied (e.g. noisy record), because the condition “Is the ventricular peak absent (nan)? ”.
Finally, MAP C, dangerous, is chosen as first one if there’s a peak into the His bundle.
Is the ventricular peak absent (nan)?
Is the ventricular peak lower than atrial one?
OR

## Slide 13: Code functioning
The given record is divided into three segments and the modulus is taken
  Atrial phase: abs(record[t=0 : t=0.35])
  Ventricular phase: abs(record[t=0.45 : t=t_end])
  His phase: abs(record[t=0.35 : t=0.45])
Then the prominence is evaluated as mult_factor times (5) the SD of the segment (plot on the right: tuning of mult_factor on the training set)
  E.g., prominence_value=mult_factor*sd(atrial_phase)
Function find_peaks is used to find peaks inside each segment. If multiple peaks are found, the highest one is chosen:
  E.g., atrial_peaks=find_peaks(atrial_phase, prominence_value)
  If the list of peaks is empty, the peak value is set to NaN
Finally, the three peaks are compared:
  If not(isnan(his_peak))  MAP_C
  Elif [atrial_peak>vent_peak OR isnan(vent_peak)]  MAP_A
  Else  MAP_B

## Slide 14: Find peaks function documentation
NB: if find_peaks return [], the algorithm will assign nan value to the peak

## Slide 15: Outline
Why building a heuristic classifier
Knowledge on roving signals: recap
Heuristic classifier: pseudo code
Performance
Conclusions

## Slide 16: Correctly classified example 1
MAP A correctly classified
The algorithm recognize as majoritarian the atrial peak (in modulus)
Grey dashed lines: his bundle peak searching area

## Slide 17: Correctly classified example 2
MAP B correctly classified
Higher ventricular peak is used to correctly assign this signal to map B.
Grey dashed lines: his bundle peak searching area

## Slide 18: Correctly classified example 3
MAP C correctly classified
His bundle is correctly recognized and used to classify this signal into MAP C.
Grey dashed lines: his bundle peak searching area

## Slide 19: Misclassified example 1
MAP A classified as MAP B
The algorithm captures the uncertainty given by the clear Map B characteristics of the signal
Grey dashed lines: his bundle peak searching area

## Slide 20: Misclassified example 2
MAP C classified as MAP B
The algorithm cannot recognize the His peak, which isn’t even clearly visible by visual inspection
Grey dashed lines: his bundle peak searching area

## Slide 21: Misclassified example 3
MAP C classified as MAP A
His bundle conduction is not clearly visible and the algorithm collects this signal into MAP A because of the higher atrial peak
Grey dashed lines: his bundle peak searching area

## Slide 22: Heuristic classifier: results on original signals
Performance have been evaluated using confusion matrix and standard metrics

## Slide 23: Heuristic classifier: results on filtered signals
Performance have been evaluated using confusion matrix and standard metrics

## Slide 24: Heuristic classifier: results on train set
 | Precision | Recall | F1-score | support
Map A | 0.94 | 0.36 | 0.53 | 557
Map B | 0.20 | 0.87 | 0.32 | 84
Map C | 0.30 | 0.49 | 0.38 | 85
Accuracy |  |  | 0.44 | 726
Macro avg | 0.48 | 0.58 | 0.41 | 726
Weighted avg | 0.78 | 0.44 | 0.48 | 726

## Slide 25: Heuristic classifier: results on test set
 | Precision | Recall | F1-score | support
Map A | 0.96 | 0.27 | 0.42 | 239
Map B | 0.16 | 0.86 | 0.27 | 36
Map C | 0.39 | 0.57 | 0.46 | 37
Accuracy |  |  | 0.37 | 312
Macro avg | 0.50 | 0.57 | 0.38 | 312
Weighted avg | 0.80 | 0.37 | 0.41 | 312

## Slide 26: Outline
Why building a heuristic classifier
Knowledge on roving signals: recap
Heuristic classifier: pseudo code
Performance
Conclusions

## Slide 27: Conclusions
A heuristic classifier has been built with the purpose to act as baseline from which starting further evaluations.
In general, performance are not satisfying, as it could be imaged.
Looking at the confusion matrices and metrics, in both train and test sets:
MAP A has many FN classified as MAP B, probably due to ambiguous signals present into this class. Only temporal-spatial information is not sufficient to classify these signals properly. This situation is reflected by the good precision juxtaposed, however with low recall.
MAP B il classified well in terms or recall, but suffers of very low precision, because of the presence MAP A misclassified signals.
MAP C suffers of both bad precision and bad recall, leading to a very low f1-score. Such situation reflects the fact that maybe the algorithm is not able to find properly the His peak or using only this information is not sufficient.
Moreover, filtered data does not have difference with not filtered ones in terms of performances.
In conclusion the presented set of rules is a simple classifier, which can be used as baseline to start the classification with a true machine learning model.